## Slide 1: Choosing The Right Processor for your Embedded System Design
EMBEDDED SYSTEM DESIGN & IoT-Master Class
DAY 2

## Slide 2
What You will learn Today?
Difference between Mp/Mc DSP,CPLD,FPGA and SoC
Selection of Packages
Processor Selection Criteria
Hardware Design Flow
Software Design Flow
Simulation , Evaluation and Emulation

## Slide 3: Day 2 Choosing the Right Processor for Embedded System Design

## Slide 4: Mindset Lesson for the Day
Rebooting Your Brain
Exercise 1 – Write down everything that you can think of that you need to do
Exercise 2- Write down everything that you can think of that you want in your life that currently you don’t have
Exercise 3- Write down everything that you can think of that you are afraid of or worry about .next to each one make a note of what a worst case scenario would be

## Slide 5: Types of Processors and Controllers
Microprocessors/
Microcontrollers (8/16/32)
DSP
CPLD/FPGA
GENERAL PURPOSE
PROCESSORS
(CPU Vs GPU)
Dallas,philips
Renesas,freescale,
Texas,Microchip
Xilinx,Altera
Lattice,Actel
Intel,AMD,Nvidia
Texas,analog devices,Motorolla,
INTEL
QUALCOMM
BROADCOMM
ASIC
SOC

## Slide 6: Microprocessor Basic
Microprocessor, must have external peripherals to
Interact with outside world,It is obsolete
CPU
CONTROL
ADDRESS
DATA
BOOT ROM
Used at startup
Instruction (program) ROM
Transducers
Keyboard Screen UART Parallel interface
etc
Data RAM

## Slide 7: Micro controller
UART
CPU
Parallel Port
Program Memory
Data Memory
Timers
ADC
CAN

## Slide 8
Digital Signal Processor is mathematics on chip.
DSPs usually run applications with hard real-time constraints:
DSPs usually process infinite continuous data streams.
MAC Capability
DSP processors are microprocessors designed for efficient
mathematical manipulation of digital signals.
Basic Features of DSPs

## Slide 9: Why do we need DSP processors?
Microcontrollers are control oriented ,DSP are data path oriented
Use a GPP processor when the following are required:
  Large memory.
  Advanced operating systems.
Use a DSP processor when the following are required:
  Precision
  Cost saving.
  Smaller size.
  Low power consumption.
  Processing of signals in real-time.

## Slide 10: CPLD Vs FPGA

## Slide 11: Diff between PLA,PAL,PLD,CPLD and FPGA

## Slide 12: CPLD Architecture
Logic blocks
I/O blocks
Clock routing
Routing matrix

## Slide 13: FPGA Architecture
I/O blocks
Clock routing
Routing matrix
Memory
Multipliers /DSP blocks
Processor core
Logic blocks

## Slide 14: FPGA Technologies

## Slide 15: DSP Vs FPGA

## Slide 16: Fine-Grained Parallelism of Special-Purpose Circuits
Example -- Calculating gravitational force:
8 instructions on a CPU → 8 cycles**
Much fewer cycles on a special purpose circuit
A = G × m1
B = A × m2
C = x1 - x2
D = C2
E = y1 - y2
F = E2
G = D + F
Ret = B / G
A = G × m1 × m2
B = (x1 - x2)2
C = (y1 - y2)2
D = B + C
Ret = B / G
4 cycles with basic operations
3 cycles with compound operations

## Slide 17: When to use DSP in FPGA
Higher Performance
Parallel algorithm implementation
Customizable Design
Optimize for speed and cost
System Integration
Less board real estate
Less chips could mean less system cost

## Slide 18: Traditional embedded system design using DSP
Power Supply
CLK
CLK
CLK
custom IF-logic
SDRAM
SDRAM
SRAM
SRAM
SRAM
Memory Controller
UART
LC
Display Controller
Interrupt Controller
Timer
Audio Codec
CPU (uP / DSP)
Co- Proc.
GP I/O
Address Decode Unit
Ethernet MAC

## Slide 19
Next Step...
FPGA
CLK
CLK
CLK
custom IF-logic
SDRAM
SDRAM
SRAM
SRAM
SRAM
Memory Controller
UART
Display Controller
Timer
Power Supply
LC
Audio Codec
CPU (uP / DSP)
Co- Proc.
GP I/O
Address Decode Unit
Ethernet MAC
Interrupt Controller

## Slide 20: Configurable system on Chip-CSoC
Power Supply
SDRAM
SDRAM
SRAM
SRAM
SRAM
LC
Audio Codec
EPROM

## Slide 21: Multicore Processor -SoC
2 or More Independent Processors in 1 Package
Symmetric Multiprocessing
  Number of Identical Processors
  Common Shared Memory
  One Operating System
Asymmetric Multiprocessing
  Different Processors, Instruction Sets
  Different Operating Systems
  Possibly Without Shared Memory

## Slide 22: AMP-TI OMAP
Processors Need Not be Identical
Processor Specialization May Increase Performance.
T.I.’s OMAP•General Purpose Processor+Digital Signal Processor(“DSP”)

## Slide 23: How FPGA Is Different From ASICs
ASIC (Application-Specific Integrated Circuit)
  Special chip purpose-built for an application
  E.g., ASIC bitcoin miner, Intel neural network accelerator
  Function cannot be changed once expensively built
+ FPGAs can be field-programmed
  Function can be changed completely whenever
  FPGA fabric emulates custom circuits

## Slide 24: Comparison
Micro controllers
DSP
FPGA
ASIC
Cost
Performance
SOC

## Slide 25: Selection of packages
QFP
SOLDERING
IRON
SOLDERING
STATION
OVEN
DIP
SOIC
BGA
PLCC

## Slide 26: Processor selection Criteria
Development tools
Number of I/O’s
Performance
Cost
Operating systems
Hardware tools
Peripherals
Power consumption
Supplier reputation

## Slide 27: Hardware Design Flow
SCHEMATIC DESIGN
LAYOUT DESIGN
ASSEMBLY & TESTING

## Slide 28: Schematic Design Consideration
Power supply design (Webench designer TI)
Use Ground Splitting if the Design contains any analog Parts(High speed ADC and DAC)
Proper Calculation of Decoupling Capacitors for VCC
ESD protection Diodes for esd sensitive IC’s

## Slide 29: Layout Design Considerations
Check Footprints
Placement of Components as per schematics
Placement of decoupling capacitors close to VCC
Length Matching for High Speed Memories
Avoid Right angle traces during routing
Place High speed memory close to the Processor

## Slide 30
Software Design Flow

## Slide 31
Simulation
Evaluation
Emulation

## Slide 32: Cabinet design
3D Printer
Laser cutting CNC

## Slide 33: Test JIG

## Slide 34
Testing
Decide application, Features,
cost of the product
Select the right processor
and packages
Design and fabricate PCB
Components Assembly
Choose Idea
C/ASM/GRAPHICAL
Integration
Recap of Designing an Embedded System

## Slide 35: Thank You